## Slide 1
NDSS PAPER UPDATE
RV-MalTrace
What should the group believe after this update?
Scope: controlled Genesys2/CVA6 tracing and semantic reconstruction. Not a malware detector or production transport claim.
artifact root: results/evaluation/genesys2-cva6/current
TRACE
EVENTS
FIRST
Notes: 周会目标：不是复述论文结构，而是让听众能回答研究问题、价值、当前结论、证据、边界和下一步判断。

## Slide 2
SIX QUESTIONS
02
The report has to answer six questions
Every slide should help answer one of them.
Q1
Research problem: low-level trace must support high-level behavior claims
Q2
Why it matters: software references are visible and must not be the only evidence path
Q3
Core conclusion: controlled reconstruction works; detector accuracy is not claimed
Q4
Evidence: trace tests, source labels, attribution fixtures, board windows, repro checks
Q5
Boundary: no real-malware accuracy, production transport, or cycle-overhead claim
Q6
Decision needed: what claim is worth submitting, and which gap to close next?
Notes: 把导师/同学带到同一条判断链上：先明确问题和价值，再给结论、证据、边界，最后请大家判断下一步。

## Slide 3
RESEARCH PROBLEM
03
What is the research problem?
Hardware trace is low-level; malware behavior claims are high-level.
SOFTWARE OBSERVER
Rich semantics
Useful reference data, but visible to the workload.
OUT-OF-BAND TRACE
Hardware path
Commit-time trace starts below user-mode observer checks.
Notes: 问题不是能不能记录事件，而是能否把低层硬件事件连接到进程、可执行文件和行为标签，同时不把参考日志误报成硬件恢复结果。

## Slide 4
MOTIVATION
04
Why is this worth studying?
Software logs are useful references, but they are part of the measured system.
OBSERVATION
Software traces are visible
They are excellent references, but adversarial workloads can observe or react to them.
INTERPRETATION
Hardware events are not behavior
A PC, trap, or syscall transition still needs process and executable context.
EVIDENCE
Sources can be confused
Reference logs must validate results without being reported as hardware output.
Notes: 价值要讲清楚：软件 tracing 不是没用，而是不适合单独承担对抗性 workload 的全部证据链；硬件 trace 提供独立观察点，但必须补上归因和边界。

## Slide 5
CURRENT CONCLUSION
05
What is the current core conclusion?
RV-MalTrace supports controlled behavior reconstruction, not detector accuracy.
Current conclusion
For controlled RISC-V Linux workloads, RV-MalTrace can reconstruct behavior summaries from CVA6 trace records while labeling supporting evidence sources.
SUPPORTED
trace ordering, syscall pairing, source labels, code attribution, reproducibility
NOT CLAIMED
real-malware accuracy, payload equivalence, production throughput, cycle overhead
Notes: 当前结论要一句话说完：在受控 RISC-V Linux workload 下，可以从 CVA6/Genesys2 trace 到 source-labeled reconstruction；不能声称真实 malware accuracy。

## Slide 6
EVIDENCE MAP
06
Which evidence supports the conclusion?
The evidence is useful only if each claim keeps its source and scope.
TRACE
Directed tests support event ordering and syscall entry/return pairing
SOURCE
Reconstruction summaries mark hardware, ELF, runtime-map, and reference fields
ATTRIB.
Local fixtures cover PIE/ASLR, dynamic objects, fork/exec, stripped binaries
BOARD
122 accepted CVA6 windows support scoped empirical claims
REPRO
Manifest and SHA-256 checks make the current evidence package reviewable
Notes: 这页是周会的证据地图：不要先堆图，而是先告诉听众每类证据支持什么，不支持什么。

## Slide 7
SYSTEM MECHANISM
07
How does the evidence flow?
Trace records, code maps, runtime maps, and references stay separate.
trace
board events
code map
local ELF view
join
PC + process scope
graph
semantic events
rules
behavior labels
SEPARATE
hardware trace is kept separate from reference labels
TAG
code and behavior claims carry source labels
Notes: 实现页只服务证据逻辑：哪些字段来自硬件 trace，哪些来自 ELF/runtime map，哪些只是 reference log。

## Slide 8
EVIDENCE DETAIL
08
Evidence 1: trace correctness
The trace contract is tested before semantic claims are made.
CONTROL
retire, branch, jump
SYSCALL
entry and qualified return
CONTEXT
trap, CSR, SATP, privilege
ACCOUNT
ARG_MEM, marker, drop records
Notes: 先证明 trace contract：事件顺序、trap/retire、syscall entry/return、drop accounting。不要直接跳到 malware behavior。

## Slide 9
EVIDENCE DETAIL
09
Evidence 2: source-labeled reconstruction
Derived fields are marked as hardware, ELF, runtime map, or reference.
hardware trace
event sequence, traps, syscall transitions
ELF metadata
binary identity, sections, symbols
runtime map
process scope and loaded objects
reference log
expected behavior for comparison
The point is not more labels; it is preventing reference evidence from being reported as hardware recovery.
Notes: 回答图表证明了什么：证明 reconstruction 没有把 reference log 当成 hardware output。

## Slide 10
EVIDENCE DETAIL
10
Evidence 3: code attribution
ELF identity, symbols, syscall sites, and runtime maps constrain attribution.
CODE MAP
ELF identity
hash, load ranges, sections, symbols
JOIN
Trace to code
PC evidence plus process/runtime scope
LIMITATION
No source-line claim
DWARF/source-line attribution needs board evidence
Notes: 说明本地 code attribution 支持哪些边界：PIE/ASLR、dynamic object、fork/exec、stripped binary；但不声称 board-native source-line attribution。

## Slide 11
EVIDENCE DETAIL
11
Evidence 4: board runs
122 accepted CVA6 windows support scoped empirical claims.
122
accepted board runs
12
samples
126
attempts
4
failed retained
0
drops / wraps / gaps
Notes: 把 122 作为目前最强的 CVA6 empirical result，同时说明 4 failed retained、0 drops/wraps/gaps in accepted windows。

## Slide 12
EVIDENCE DETAIL
12
Evidence 5: controlled workloads
The workload set checks behavior reconstruction, not real-world coverage.
safe baseline
4 samples
42 accepted reps
surrogate
8 samples
80 accepted reps
benign controls
5 samples
scoped controls
Notes: 明确 workload 的用法：controlled behavior coverage，而不是 in-the-wild malware benchmark。

## Slide 13
EVIDENCE DETAIL
13
Evidence 6: behavior checks
Perfect scoped metrics validate reconstruction, not detector accuracy.
1.0
syscall recall
1.0
precision
1.0
argument recon.
0.0
benign FPR
Controlled workload analysis only. Not detection accuracy.
Notes: 这页必须带红线：1.0/0.0 的指标不能被听众理解成检测器准确率。

## Slide 14
BOUNDARY
14
What are the boundaries?
Unsupported topics stay as limitations or future work.
WRITE
hardware-assisted behavior tracing and analysis
WRITE
35T end-to-end prototype; scoped CVA6 evidence
LIMIT
synthetic and safety-controlled malware-derived behaviors
DO NOT
real-malware accuracy, payload equivalence, production detector
Notes: 这页回答证据边界：real malware、production transport、cycle overhead、JTAG RAM boot 不能放进当前主结论。

## Slide 15
ALTERNATIVE EXPLANATIONS
15
What else could explain the result?
The current evidence rules out some failures, but not all external validity concerns.
ALT 1
Reference logs may supply too much semantic information; source labels expose that boundary
ALT 2
Local code-attribution fixtures may not equal board-native source-line evidence
ALT 3
Controlled workloads may not predict in-the-wild malware behavior coverage
ALT 4
Resource deltas do not establish runtime slowdown without cycle-overhead measurement
Notes: 博士周会要主动讲替代解释：是不是 software reference 帮太多？是不是 local fixture 不等于 board evidence？是不是 controlled workload 太窄？

## Slide 16
COST
16
What cost is measured?
Resource and timing evidence support implementation cost, not runtime slowdown.
LUT
+25.32%
FF
+16.18%
BRAM18
+5.56%
DSP
+0.00%
Timing MET, slack 0.177 ns. Cycle-level runtime overhead remains unsupported.
Notes: 成本页保留，但必须说清楚：resource delta and timing closure，不是 cycle-level overhead。

## Slide 17
NEXT STEP
17
What should the group help decide?
The next work is not more running; it is claim selection and one evidence gap.
DECIDE
Is the submission claim trace-backed behavior reconstruction, not malware detection?
DECIDE
Which single evidence gap matters most: board-native source lines, overhead, or transport?
CUT
Move real-malware accuracy and payload-equivalence claims to limitations/future work
NEXT
Convert remaining prose claims into final figures and claim-evidence tables
Notes: 最后必须给导师可判断的问题：主 claim 是否足够，是否补一个 board-native evidence，哪些 nonclaims 放 limitations。

## Slide 18
REPRODUCIBILITY
18
The artifact package is reviewable
The paper should cite reproducible evidence, not untracked experiment memory.
MANIFEST
current artifact root accepted
ARCHIVE
3160 files, 316.9 MB, SHA d5b806...433b
CHECKERS
repro:quick and documented full gates pass
PAPER
NDSS draft builds; figures and quantitative tables still need final polish
Notes: reproducibility 不再作为项目管理状态，而是作为证据可信度的一部分。

## Slide 19
TAKEAWAY
19
Paper narrative
Problem -> conclusion -> evidence -> boundary -> decision.
Problem
trace to behavior
Conclusion
controlled recon.
Evidence
tests + board
Decision
claim + gap
Notes: 收尾把六问串起来，不再停在“这周做了哪些事情”。

## Slide 20
APPENDIX
20
Streaming/DMA remains future work
Readiness and target profiles are not throughput evidence.
TARGET
p99 = 0.0215755 event bytes/cycle
REQUIRED
0.0323633 event bytes/cycle, about 1.618 MB/s at 50 MHz
CURRENT
sustained streaming = 0; noninterference = false
Notes: target p99 0.0215755 B/cycle; required 0.0323633 B/cycle; at 50 MHz required 1.618 MB/s; current sustained=0, noninterference=false。

## Slide 21
APPENDIX
21
Workload roster
Sample names are appendix material, not main-story material.
SAFE
hello_write; file_open_read_write; fork_exec; illegal_instruction
SURROGATE
file_scan; batch_open_read_write; self_copy_sim; abnormal_syscall_sequence
SURROGATE
illegal_trap; process_chain; dynamic_executable_memory; anti_debug_like
BENIGN
hello; cat; clock_status; getdents_only; mmap_rw
Notes: 列出 safe baseline、malware-behavior surrogates、benign controls。长样本名只放在附录，不进入主线叙事。

## Slide 22
APPENDIX
22
Resource detail
Resource/timing claim is supported; runtime overhead is not.
LUT
FF
BRAM18
DSP
baseline
84,923
56,491
108
27
trace
106,428
65,634
114
27
delta
+25.32%
+16.18%
+5.56%
+0
Notes: baseline vs trace-enabled resource table。